## Slide 1: proposed amendments to Rule 2001 and rule 2002
Regulation XX (RECLAIM)
PUBLIC WORKSHOP
AUGUST 9, 2018

## Slide 2: Overview of PARs 2001 & 2002
PAR 2001
  Introduces an opt-out provision for facilities that meet the criteria to exit RECLAIM
    Criteria and procedures are established
PAR 2002
  Revises the criteria for facilities to be eligible to exit RECLAIM (original criteria adopted in January 5, 2018 amendments)
  Introduces an option for facilities to remain in RECLAIM upon receiving an initial determination notification for potential exit
  Introduces new temporary provision for exiting RECLAIM facilities regarding NSR offsets

## Slide 3: January 5, 2018 Amendments
Initiated the process to transition facilities out of RECLAIM
PAR 2001
Prohibited any facilities from entering RECLAIM
PAR 2002
Established notification procedures for facilities that were identified as ready to exit RECLAIM
Established criteria for facilities to be identified as eligible to exit
Addressed RTC holdings for exited facilities

## Slide 4: Background (continued)
Staff initially identified 37 RECLAIM facilities for potential exit, based on Rule 2002 criteria
Some facilities did not receive an Initial Determination Notification as part of this initial group
  Others have shut down equipment and no longer operate RECLAIM sources

## Slide 5: PAR 2001
Establishes eligibility criteria for facilities to opt-out of RECLAIM
Establishes procedures for facilities to opt-out of RECLAIM

## Slide 6: PAR 2001 – Opt-Out
Facilities may request to opt-out of RECLAIM provided that they meet certain criteria
A facility is not eligible to opt-out if it operates:
  NOx emitting equipment that is explicitly categorized in a non-RECLAIM command-and-control NOx rule that exempts RECLAIM facilities; and/or
  Non-combustion NOx emitting equipment that is not explicitly listed in any non-RECLAIM rule
Facilities cannot exit unless all facility equipment is subject to a command-and-control rule that establishes BARCT emissions limits, BARCT implementation schedules, and MRR requirements for the transition to command-and-control
In other words…

## Slide 7: PAR 2001 Opt-Out Procedures
If the facility meets the criteria, it may submit a request to the Executive Officer
Facility is required to submit with the request:
  A listing of all permitted and unpermitted NOx RECLAIM equipment, including applicable control equipment; and
  Permitted NOx emission levels, and if not available, manufacturer guaranteed NOx emission levels for the equipment
If approved, facility would receive an initial determination notification and be subject to provisions in Rule 2002 for exiting

## Slide 8: PAR 2002
Revises eligibility criteria for facilities to be identified as ready to exit
Establishes an option for facilities to remain in RECLAIM if issued an initial determination notification
Adds provision for exiting facilities regarding NSR offsets
Removes provision requiring reporting of infinite year block NOx RTC (IYB) prices

## Slide 9: Revised Eligibility Criteria to Exit
Revised Criteria
Facility does not have NOx emitting equipment that is subject to a non-RECLAIM rule that regulates NOx emissions and exempts such NOx emitting equipment
Facility does not have non-combustion NOx equipment that has no applicable non-RECLAIM rule that pertains to such NOx emissions
Old Criteria
Facility has emissions from Rule 219 equipment, unless the equipment would be subject to a command-and-control rule that it cannot reasonably comply with, equipment with various location permits, or unpermitted equipment
Facility’s NOx RECLAIM equipment meets current command-and-control BARCT rules
    Facilities do not need to be at BARCT to exit
    However, all facility equipment must be subject to a non-RECLAIM NOx emissions limiting rule (Facilities will be subject to these rules when rules are amended and no longer exempt RECLAIM facilities)
    If there is no non-RECLAIM rule applicable to a piece of equipment, the facility may not exit
What Changed?

## Slide 10: Revised Eligibility Criteria Applicability
All facilities in RECLAIM, including the 37 facilities that have received initial determination notifications, cannot exit unless they meet the revised criteria
  Even if facilities have already received an initial determination notification
As command-and-control rules are adopted/amended, more groups of facilities would meet the criteria to exit
  Even if equipment is currently not complying with a future BARCT limit, it would be subject to that applicable rule’s implementation schedule

## Slide 11: Eligible Facilities
Facilities that would be eligible to exit would have:
  No NOx emitting equipment
  NOx emissions from only Rule 219 equipment (excluding equipment subject to Rule 1146.2)
  Equipment subject to a non-RECLAIM rule that does not exempt RECLAIM facilities or is not listed in Table 1 in Rule 2001 (i.e., Facilities with only Rule 1470 equipment)

## Slide 12: Examples
Facility
Facility
Cannot Exit
Rule 219
Rule 1146.2
Exempts RECLAIM Facilities
Exit
Facility has only Rule 219 equipment – facility may exit
Facility has Rule 219 equipment and Rule 1146.2 equipment – facility may NOT exit
Rule 219

## Slide 13: Examples
Facility
Facility
Cannot Exit
Non-Refinery Flares
Rule 1146
AMENDED Includes RECLAIM Facilities
Exit
Facility has Rule 1146 equipment and equipment that would be subject to Proposed Rule 1118.1 – Non-Refinery Flares
Facility may NOT exit until a Rule 1118.1 is adopted
Rule 1146
AMENDED Includes RECLAIM Facilities
No Rule
Rule 1118.1
ADOPTED
Includes RECLAIM Facilities

## Slide 14: Examples
Rule 1146
Rule 219
Facility
Exempts RECLAIM Facilities
Cannot Exit
Facility
Rule 219
Rule 1146
AMENDED
Includes RECLAIM Facilities
Exit
Facility has Rule 219 equipment and boilers that would be subject to Rule 1146, if the rule did not exempt RECLAIM facilities: If Rule 1146 has not been amended to include RECLAIM facilities, the facility may NOT exit
Once Rule 1146 is amended to include RECLAIM facilities – the facility may exit

## Slide 15: Examples
Facility
Cannot Exit
Facility
AMENDED
Includes RECLAIM Facilities
Exit
Facility has equipment that would be subject to Rule 1146 and 1147 if they did not exempt RECLAIM facilities: Rule 1146 has been amended to include RECLAIM facilities but Rule 1147 has not been amended yet; the facility may NOT exit.
Once Rule 1147 is amended – the facility may exit
Rule 1146
Rule 1147
Exempts RECLAIM Facilities
Rule 1146
AMENDED
Includes RECLAIM Facilities
Rule 1147
AMENDED Includes RECLAIM Facilities

## Slide 16: Examples
Facility
Cannot Exit
AMENDED
Includes RECLAIM Facilities
Facility has equipment that is subject to amended rules that do not exempt RECLAIM facilities and has a piece of equipment in which there is no rule to comply with (e.g., nitric acid tanks); the facility may NOT exit.
Rule 1146
Rule 1147
AMENDED Includes RECLAIM Facilities
Rule 219
No Rule

## Slide 17: Examples
Facility
Cannot Exit
Facility has Rule 1146 equipment and Rule 1147 equipment: If Rule 1147 has not been amended to include RECLAIM facilities, but the facility shuts down their Rule 1147 equipment, the facility may exit
Rule 1146
Rule 1147
Facility
AMENDED
Includes RECLAIM Facilities
Exempts RECLAIM Facilities
Exit
Rule 1146
AMENDED
Includes RECLAIM Facilities
Rule 1147
SHUTDOWN

## Slide 18: Option to Remain in RECLAIM
Stakeholders expressed concerns about transitioning before Regulation XIII – New Source Review is amended
PAR 2002 will allow facilities to remain in RECLAIM for a limited time while NSR issues are resolved
Applies to facilities that receive an initial determination notification
  Facility submits request to remain in RECLAIM, along with equipment information required in the initial determination notification
  Executive Officer will notify the facility that it will remain in RECLAIM until a future date, but no later than December 31, 2023

## Slide 19: Provisions for Remaining in RECLAIM
Facilities that remain in RECLAIM:
  Would be required to comply with all requirements of any applicable non-RECLAIM rule that does not exempt RECLAIM facilities
    A facility will be subject to BARCT requirements of a non-RECLAIM command-and-control rule while remaining in RECLAIM
  The facility will remain in RECLAIM until a subsequent notification is issued stating the date that the facility will exit
  Upon subsequent notification, a facility will submit any updated NOx equipment information to the Executive Officer

## Slide 20: Exiting Facilities
  PAR 2002 adds a new provision for exiting facilities to provide a temporary pathway for facilities to exit, despite unresolved NSR issues
  NSR Issues:
    Permit moratorium - Rule 1315 contains cumulative net emissions increase thresholds
    Potential impacts from exiting RECLAIM facilities were not analyzed for Rule 1315 CEQA thresholds
      Will be the subject for future Regulation XIII amendments

## Slide 21: Additional Provision for Exiting Facilities
    PAR 2002 would allow facilities that meet specified criteria to exit
    Exited facilities can use ERCs in open market once exited
    Added provision to prohibit use of internal bank
      Concerns for potentially exceeding CEQA thresholds
      Could possibly result in a permit moratorium

## Slide 22: Reporting Infinite Year Block (IYB) Prices
  Rule 2002 contains a provision that requires the Executive Officer to report to the Governing Board if IYB prices fall below $200,000
    Adopted as part of the 2015 RECLAIM amendments
    Prices fell below $200,000 in September 2017
    RECLAIM transition has resulted in a sharp decrease of IYB trading
  PAR 2002 would remove this reporting requirement

## Slide 23: Rulemaking Schedule
Written Comments Deadline
  August 23, 2018
30-Day Documents
  September 4, 2018
Set Hearing
  September 7, 2018
Working Group Meeting
  September 13, 2018
Stationary Source Committee Meeting
  September 21, 2018
Public Hearing
  October 5, 2018

## Slide 24: Contacts
Melissa Gamoning Assistant Air Quality Specialist (909) 396-3115 mgamoning@aqmd.gov
Kevin Orellana Program Supervisor (909) 396-3492 korellana@aqmd.gov
Gary Quinn, P.E. Program Supervisor (909) 396-3121 gquinn@aqmd.gov
Tracy A. Goss, P.E. Planning and Rules Manager (909) 396-3106 tgoss@aqmd.gov